## Slide 1: CSC 3210 Computer Organization and Programming
Dr. Zulkar Nine
mnine@gsu.edu
Georgia State University
Spring 2021
Chapter 4: Data Transfers,
Addressing, and Arithmetic

## Slide 2: Outline
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions

## Slide 3: Data Transfer Instructions
Operand Types
Instruction Operand Notation
Direct Memory Operands
MOV Instruction
Zero & Sign Extension
XCHG Instruction
Direct-Offset Instructions

## Slide 4: Data Transfer Instructions: Operand Types
Immediate – a constant integer (8, 16, or 32 bits)
  value is encoded within the instruction
Register – the name of a register
  register name is converted to a number and encoded within the instruction
Memory – reference to a location in memory
  memory address is encoded within the instruction, or a register holds the address of a memory location
00000000 .data
00000000 00000000 sum DWORD 0
00000000 .code
00000000 main proc
00000000 B8 00000008 mov eax, 8 00000005 83 C0 04 add eax, 4 00000008 A3 00000000 R mov sum, eax
Listing File

## Slide 5: Data Transfer Instructions: Instruction Operand Notation
MOV reg,reg
MOV mem,reg
MOV reg,mem
MOV mem,imm
MOV reg,imm

## Slide 6: Data Transfer Instructions
Register to Register
Register to Memory , Vice versa
0011010
0011012
0011014

## Slide 7: How to see variables in VS

## Slide 8: Data Transfer Instructions: Direct Memory Operands
A direct memory operand is a named reference to storage in memory
.data
var1 BYTE 10h
.code
mov al,var1 ; AL = 10h
mov al,[var1] ; AL = 10h
alternate format

## Slide 9: Data Transfer Instructions: Direct Memory Operands
The named reference (label) is automatically dereferenced by the assembler
.data
var1 BYTE 10h
Suppose var1 were located at offset 10400h.
The following instruction copies its value into the AL register:
mov al, var1
It would be assembled into the following machine instruction:
A0 00010400

## Slide 10: Data Transfer Instructions: Direct Memory Operands
The named reference (label) is automatically dereferenced by the assembler
A0 00010400
- The first byte in the machine instruction is the opcode.
- The remaining part is the 32-bit hexadecimal address of var1.
00000000 .data
00000000 00000000 sum DWORD 0
00000000 .code
00000000 main proc
00000000 B8 00000008 mov eax, 8 00000005 83 C0 04 add eax, 4 00000008 A3 00000000 R mov sum, eax
Listing File

## Slide 11: Data Transfer Instructions: MOV Instruction
.data
count BYTE 100
wVal WORD 2
.code
mov bl,count
mov ax,wVal
mov count,al
mov al,wVal ; error
mov ax,count ; error
mov eax,count ; error
Move from source to destination.
Syntax:
    MOV destination, source
MOV instruction formats:
  Both operands must be the same size.
  Both operands cannot be memory operands.
  The (IP, EIP, or RIP) cannot be a destination operand.
Ex:
MOV reg,reg
MOV mem,reg
MOV reg,mem
MOV mem,imm
MOV reg,imm

## Slide 12: Data Transfer Instructions: MOV Instruction
Explain why each of the following MOV statements are invalid:
size mismatch
.data
bVal BYTE 100
bVal2 BYTE ?
wVal WORD 2
dVal DWORD 5
.code
mov ds,45
mov eax,wVal
mov eip,dVal
mov 25,bVal
mov bVal2,bVal
immediate move to DS not permitted
EIP cannot be the destination
immediate value cannot be destination
memory-to-memory move not permitted
Both operands must be the same size.
Both operands cannot be memory operands.
The (IP, EIP, or RIP) cannot be a destination operand.

## Slide 13: Data Transfer Instructions: MOV Instruction
Memory to Memory (problem):
  A single MOV instruction cannot be used to move data directly from one memory location to another.
  Instead, you must move
    the source operand’s value to a register
    before assigning its value to a memory operand:
.data
var1 WORD ?
var2 WORD ?
.code
mov ax,var1
mov var2,ax
Ex:
Notes: Sec09 Feb14th

## Slide 14: Data Transfer Instructions: MOV Instruction
.data
oneWord WORD 1234h
oneDword DWORD 12345678h
Overlapping Values
The same 32-bit register can be modified using differently sized data.
  When oneWord is moved to AX, it overwrites the existing value of AL.
  When oneDword is moved to EAX, it overwrites AX.
  When 0 is moved to AX, it overwrites the lower half of EAX.
.code
mov eax, 0
mov ax, oneWord ; EAX = 00001234h
mov eax, oneDword ; EAX = 12345678h
mov ax, 0 ; EAX = 12340000h
Notes: Sec 06, Feb 15

## Slide 15: Data Transfer Instructions: Zero & Sign Extension
Sign extension problem:
MOV cannot directly copy data from a smaller operand to a larger one
Workarounds:
Suppose count (unsigned, 16 bits) must be moved to ECX (32 bits).
Trick: Set ECX to zero and move count to CX:
What happens if we try the same approach with a signed integer equal to -16?
00000000000000000000000000000000
0000000000000001
cx
ch
cl
ecx
00000000000000000000000000000001
ecx

## Slide 16
00000000000000000000000000000000
0000000000000001
cx
ch
cl
ecx

## Slide 17: Data Transfer Instructions: Zero & Sign Extension
Sign extension problem:
What happens if we try the same approach with a signed integer equal to -16?

## Slide 19: Data Transfer Instructions: Zero & Sign Extension
Sign extension problem:
If we had filled ECX first with FFFFFFFFh and then copied signedVal to CX:
mov ecx,FFFFFFFFh
mov cx,signedVal ; ECX = FFFFFFF0h (-16)
MOVZX and MOVSX instructions to deal with both unsigned and signed integers.
11111111111111111111111111111111
1111111111110000
cx
ch
cl
ecx
11111111111111111111111111110000

## Slide 20: Data Transfer Instructions: Zero Extension (MOVZX )
The MOVZX instruction
When you copy a smaller value into a larger destination,
  the MOVZX instruction fills (extends) the upper half of the destination with zeros.
mov bl,10001111b
movzx ax,bl ; zero-extension
The destination must be a register.
ax
ah
al

## Slide 22: Data Transfer Instructions: Zero Extension (MOVZX )

## Slide 23: Data Transfer Instructions: Sign Extension (MOVSX )
The MOVSX instruction
It fills the upper half of the destination with a copy of the source operand's sign bit.
mov bl,10001111b
movsx ax,bl ; sign extension
The destination must be a register.
ax
ah
al

## Slide 24: Data Transfer Instructions: Sign Extension (MOVSX )
In the following example,
  the hexadecimal value moved to BX is A69B,
  so the leading “A” digit tells us that the highest bit is set.
mov bx, A69Bh
movsx eax,bx ; EAX = FFFFA69Bh
movsx edx,bl ; EDX = FFFFFF9Bh
movsx cx,bl ; CX = FF9Bh
Notes: TH, Sep-26, 4pm

## Slide 25: Data Transfer Instructions: Zero & Sign Extension
MOVZX vs. MOVSX
ax
ah
al
ax
ah
al
MOVZX
MOVSX

## Slide 27: Data Transfer Instructions: XCHG Instruction
XCHG exchanges the values of two operands.
  At least one operand must be a register.
  No immediate operands are permitted.
xchg ah,al ; exchange 8-bit regs
xchg ax,bx ; exchange 16-bit regs
xchg eax,ebx ; exchange 32-bit regs
xchg var1,bx ; exchange 16-bit mem op with BX
xchg var1,var2 ; error: two memory operands
Notes: Sec 03, Fe16

## Slide 29
Xchange items

## Slide 30: Data Transfer Instructions: XCHG Instruction
.data
var1 WORD 1000h
var2 WORD 2000h
.code
XCHG exchanges the values of two operands.
  At least one operand must be a register.
  No immediate operands are permitted.
mov ax,val1
xchg ax,val2
mov val1,ax

## Slide 31: Data Transfer Instructions: Direct-Offset Operands
.data
arrayB BYTE 10h,20h,30h,40h
.code
mov al,arrayB ; AL = 10h
mov al,arrayB+1 ; AL = 20h
A constant offset is added to a data label to produce an effective address (EA).
The address is dereferenced to get the value inside its memory location.
Why doesn't arrayB+1 produce 11h?
mov al,[arrayB+1] ; alternative notation
Notes: Sec-09, Feb-18

## Slide 32: Data Transfer Instructions: Direct-Offset Operands
.data
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov ax, [arrayW+2] ; AX = 2000h
mov ax, [arrayW+4] ; AX = 3000h
mov eax,[arrayD+4] ; EAX = 00000002h
Will the following statements assemble?
mov ax,[arrayW-2] ; ??
mov eax,[arrayD+16] ; ??

## Slide 34: Data Transfer Instructions: Direct-Offset Operands
.data
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov ax, [arrayD+0] ; AX = 2000h
mov ax, [arrayD+4] ; AX = 3000h
mov eax,[arrayD+8] ; EAX = 00000002h
Will the following statements assemble?
mov ax,[arrayW-2] ; ??
mov eax,[arrayD+16] ; ??

## Slide 36: Data Transfer Instructions: Direct-Offset Operands
Write a program that rearranges the values of three doubleword values in the following array as:
  1,2,3 ---------- 3, 1, 2.
  .data
  arrayD DWORD 1,2,3
Step 2: Exchange EAX with the THIRD array value and copy the value in EAX to the FIRST array position.
Step1: copy the FIRST value into EAX and exchange it with the value in the SECOND position.
xchg eax,[arrayD+8]
mov arrayD,eax
mov eax, arrayD
xchg eax, [arrayD+4]
LAB

## Slide 38: Data Transfer Instructions: Direct-Offset Operands
We want to write a program that adds the following three bytes:
.data
myBytes BYTE 80h,66h,0A5h
What is your evaluation of the following code?
mov al,myBytes
add al,[myBytes+1]
add al,[myBytes+2]
What is your evaluation of the following code?
movsx ax, myBytes
add ax, [myBytes+1]
add ax, [myBytes+2]
Any other possibilities?

## Slide 40: Outline
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions

## Slide 41: Addition and Subtraction
INC and DEC Instructions
ADD and SUB Instructions
NEG Instruction
Implementing Arithmetic Expressions
Flags Affected by Arithmetic
  Zero
  Sign
  Carry
  Overflow

## Slide 42: Addition and Subtraction: INC and DEC Instructions
Add 1, subtract 1 from destination operand
  operand may be register or memory
The Syntax:
INC destination
    Logic: destination  destination + 1
DEC destination
    Logic: destination  destination – 1

## Slide 43: Addition and Subtraction: INC and DEC Examples
.data
myWord WORD 1000h
myDword DWORD 10000000h
.code
inc myWord ; 1001h
dec myWord ; 1000h
inc myDword ; 10000001h
mov ax,00FFh
inc ax ; AX = 0100h
mov ax,00FFh
inc al ; AX = 0000h

## Slide 44: Addition and Subtraction: INC and DEC Examples
Show the value of the destination operand after each of the following instructions executes:
.data
myByte BYTE FFh, 0
.code
mov al,myByte ; AL =
mov ah,[myByte+1] ; AH =
dec ah ; AH =
inc al ; AL =
dec ax ; AX =
FFh
00h
FFh
00h
FEFF

## Slide 45: Addition and Subtraction
INC and DEC Instructions
ADD and SUB Instructions
NEG Instruction
Implementing Arithmetic Expressions
Flags Affected by Arithmetic
  Zero
  Sign
  Carry
  Overflow

## Slide 46: ADD and SUB Instructions
ADD destination, source
  Logic: destination  destination + source
SUB destination, source
  Logic: destination  destination – source
Same operand rules as for the MOV instruction

## Slide 47: ADD and SUB Examples
.data
var1 DWORD 10000h
var2 DWORD 20000h
.code ; ---EAX---
mov eax,var1 ; 00010000h
add eax,var2 ; 00030000h
add ax,0FFFFh ; 0003FFFFh
add eax,1 ; 00040000h
sub ax,1 ; 0004FFFFh
Can you add registers of different sizes?
add eax,bx
Can you add mem to mem?
add var1,var2
Notes: Sep27,Wed, 3pm

## Slide 48: Addition and Subtraction
INC and DEC Instructions
ADD and SUB Instructions
NEG Instruction
Implementing Arithmetic Expressions
Flags Affected by Arithmetic
  Zero
  Sign
  Carry
  Overflow
Notes: Sec09, Feb21
Sum 2017. Jun 22nd

## Slide 49: NEG (negate) Instruction
.data
valB SBYTE -1 ;valB BYTE -1 is also acceptable, why?
valW WORD +32
.code
mov al,valB ; AL = -1
neg al ; AL = +1
neg valW ; valW = -32
Reverses the sign of an operand.
Operand can be a register or memory operand.
Suppose AX contains –32,768 and we apply NEG to it.
Will the result be valid?
Ex.
Notes: Sep28, Thr, 9:30
Sec06, Feb27

## Slide 50: Addition and Subtraction
INC and DEC Instructions
ADD and SUB Instructions
NEG Instruction
Implementing Arithmetic Expressions
Flags Affected by Arithmetic
  Zero
  Sign
  Carry
  Overflow
Notes: Sec03, Feb 21

## Slide 51: Implementing Arithmetic Expressions
.code
mov eax,Xval
neg eax ; EAX = -26
mov ebx,Yval
sub ebx,Zval ; EBX = -10
add eax,ebx
mov Rval,eax ; -36
HLL compilers translate mathematical expressions into assembly language.
You can do it also.
  For example: Do not permit Xval, Yval, or Zval to be modified
.data
Rval SDWORD ?
Xval SDWORD 26
Yval SDWORD 30
Zval SDWORD 40
Rval = -Xval + (Yval – Zval)

## Slide 52: Implementing Arithmetic Expressions
mov ebx,Yval
neg ebx
add ebx,Zval
mov eax,Xval
sub eax,ebx
mov Rval,eax
Translate the following expression into assembly language.
  Do not permit Xval, Yval, or Zval to be modified:
Rval = Xval - (-Yval + Zval)
Assume that all values are signed doublewords.
Previous Example:
Rval = -Xval + (Yval – Zval)
.data
Rval SDWORD ?
Xval SDWORD 26
Yval SDWORD 30
Zval SDWORD 40

## Slide 53: Addition and Subtraction
INC and DEC Instructions
ADD and SUB Instructions
NEG Instruction
Implementing Arithmetic Expressions
Flags Affected by Arithmetic
  Zero
  Sign
  Carry
  Overflow

## Slide 54: Flags: Why?
When executing arithmetic instructions, we often want to know something about the result:
  Is it negative, positive, or zero?
  Is it too large or too small to fit into the destination operand?
Answers to such questions can help detect calculation errors that might otherwise cause erratic program behavior.
The values of CPU status flags is used to check the outcome of arithmetic operations.
  Status flag values are also used to activate conditional branching instructions, the basic tools of program logic.

## Slide 55: Flags: Flags Affected by Arithmetic/Bitwise
The ALU has a number of status flags that reflect the outcome of
  arithmetic operations
  bitwise operations
based on the contents of the
destination operand

## Slide 56: Flags: Flags Affected by Arithmetic/Bitwise
Essential flags:
  Zero flag – set when destination equals zero
  Sign flag – set when destination is negative
  Carry flag – set when unsigned value is out of range
  Overflow flag – set when signed value is out of range
Visual Studio Flags?
The MOV instruction never affects the flags. (Why?)

## Slide 57: Flags: Map
status flags
ALU
conditional jumps
branching logic
arithmetic & bitwise operations
part of
used by
provide
attached to
affect
CPU
executes
executes
The ALU has a number of status flags that reflect the outcome of arithmetic operations and bitwise operations.

## Slide 58: Flags: Displaying CPU Flags in Visual Studio
You must be currently debugging a program in order to see these menu options.
To display the CPU status flags during a debugging session,
  select Windows from the Debug menu,
  then select Registers from the Windows menu.
  Inside the Registers window, right-click and select Flags from the dropdown list.
Each flag is assigned a value of 0 (clear) or 1 (set).

## Slide 59: Flags: Unsigned and Signed Integers Operations
All CPU instructions operate exactly the same on signed and unsigned integers
The CPU cannot distinguish between signed and unsigned integers
The programmer, are responsible for using the correct data type with each instruction
CF vs. OF

## Slide 60: Flags: Unsigned Operations, Zero flag (ZF)
mov ecx,1
sub ecx,1 ; ECX = 0, ZF = 1
mov eax,FFFFFFFFh
inc eax ; EAX = 0, ZF = 1
inc eax ; EAX = 1, ZF = 0
The Zero flag (ZF) is set when the result of an operation produces zero in the destination operand.
Remember...
A flag is set when it equals 1.
A flag is clear when it equals 0.
Based on the contents of the destination operand
Notes: Jun.27th, Tuesday

## Slide 61: Flags: Unsigned Operations, Carry flag (CF)
The Carry flag (CF) is set when the result of an operation generates an unsigned value that is out of range (too big or too small for the destination operand).
Addition .Vs Subtraction (borrow)
mov al,0FFh
add al,1 ; CF = 1, AL = 00
Addition and the Carry Flag
Notes: For integer class numbers, "underflow" is said to occur when the value would be less than the minimum integer representable in that class.

## Slide 62: Flags: Unsigned Operations, Carry flag (CF)
Subtraction and the Carry (and borrow) Flag
A subtract operation sets the Carry flag when
  a larger unsigned integer is subtracted from a smaller one.
mov al,1
sub al,2 ; AL = FFh, CF = 1
Notes: For integer class numbers, "underflow" is said to occur when the value would be less than the minimum integer representable in that class.

## Slide 63: Flags: Unsigned Operations, Carry flag (CF)
Subtraction and the Carry (and borrow) Flag
A subtract operation sets the Carry flag when
  a larger unsigned integer is subtracted from a smaller one.
; Try to go below zero:
mov al,0
sub al,1 ; CF = 1, AL = FF
Notes: For integer class numbers, "underflow" is said to occur when the value would be less than the minimum integer representable in that class.

## Slide 64: Flags: Unsigned Operations, Parity
Parity
The Parity flag (PF) is set when
  The least significant byte of the destination has an even number of 1 bits.
The following ADD and SUB instructions alter the parity of AL:
          mov al,10001100b
          add al,00000010b ; AL = 10001110, PF = 1
          sub al,10000000b ; AL = 00001110, PF = 0

## Slide 65: Flags: Signed Operations, Sign Flag (SF)
mov cx,0
sub cx,1 ; CX = -1, SF = 1
add cx,2 ; CX = 1, SF = 0
The Sign flag (SF) is set when the destination operand is negative.
The flag is clear when the destination is positive.

## Slide 66: Flags: Signed Operations, Sign Flag (SF)
The Sign flag (SF) is set when the destination operand is negative.
The sign flag is a copy of the destination's highest bit:
mov al,0
sub al,1 ; AL = 11111111b, SF = 1
add al,2 ; AL = 00000001b, SF = 0

## Slide 67: Flags: Signed Operations, Overflow Flag (OF)
The Overflow flag (OF) is set when the signed result of an operation is invalid or out of range.
; Example 1
mov al,+127
add al,1 ; OF = 1, AL = ??
; Example 2
mov al,7Fh ; OF = 1, AL = 80h
add al,1
The two examples are identical at the binary level because 7Fh equals +127.
To determine the value of the destination operand, it is often easier to calculate in hexadecimal.
Notes: AL = 80

## Slide 68: Flags: Unsigned and Signed Integers Operations
For each of the following marked entries,
  show the values of the destination operand and the Sign, Zero, Carry , and overflow flags:
mov ax,7ff0h
add al,10h ; AX= SF= ZF= CF= OF=
add ah,1 ; AX= SF= ZF= CF= OF=
add ax,2 ; AL= SF= ZF= CF= OF=
8000  32768

## Slide 69: Flags: Unsigned and Signed Integers Operations
Use the following data for Questions 4-5:
.data
val2 WORD 8000h
val4 WORD 7FFFh
1. If val2 is incremented by 1 using the ADD instruction, what will be the values of the Carry and Sign flags?
2. If val4 is incremented by 1 using the ADD instruction, what will be the values of the Overflow and Sign flags?

## Slide 70: Flags: Unsigned and Signed Integers Operations
When adding two integers, remember that the Overflow flag is only set when . . .
  Two positive operands are added and their sum is negative
  Two negative operands are added and their sum is positive
What will be the values of the Overflow flag?
mov al,80h
add al,92h ; OF =
mov al,-2
add al,+127 ; OF =
1
0
A Rule of Thumb
Notes:   Two positive operands are added and their sum is negative
mov al,+127 add al,1 ; OF = 1, AL = ??
Overflow occurs if
(+A) + (+B) = −C
(−A) + (−B) = +C
Example: Using 4-bit Two's Complement numbers (−8 ≤ x ≤ +7)
(−7) 1001
+(−6) 1010
------------
(−13) 1 0011 = 3 : Overflow (largest −ve number is −8)

## Slide 71: Flags: Unsigned and Signed Integers Operations
What will be the values of the given flags after each operation?
mov al,-128
neg al ; CF = OF =
mov ax,8000h
add ax,2 ; CF = OF =
mov ax,0
sub ax,2 ; CF = OF =
mov al,-5
sub al,+125 ; OF =
1 1
0 0
1 0
1
Overflow and Carry Flags
?
a larger signed integer is subtracted from a smaller one
Notes: A subtract operation sets the Carry flag when
  a larger signed integer is subtracted from a smaller one.

## Slide 72: Flags: NEG Instruction
The NEG instruction produces an invalid result
  If the destination operand cannot be stored correctly.
Ex1.
- If we move 128 to AL and try to negate it, the correct value (128) will not fit into AL.
- The Overflow flag is set, indicating that AL contains an invalid value:
mov al,-128 ; AL = 10000000b
neg al ; AL = 10000000b, OF = 1

## Slide 73: Flags: NEG Instruction
The NEG instruction produces an invalid result
  If the destination operand cannot be stored correctly.
Ex2.
- If 127 is negated, the result is valid and the Overflow flag is clear:
mov al,+127 ; AL = 01111111b
neg al ; AL = 10000001b, OF = 0

## Slide 74: Flags: NEG Instruction
The NEG instruction produces an invalid result
  If the destination operand cannot be stored correctly.
Ex2.
- If 127 is negated, the result is valid and the Overflow flag is clear:
mov al,+127 ; AL = 01111111b
neg al ; AL = 10000001b, OF = 0

## Slide 75: Outline
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions
64-Bit Programming

## Slide 76: Operators and Directives
Operators and directives are not executable instructions;
  They are interpreted by the assembler.
OFFSET Operator
PTR Operator
TYPE Operator
LENGTHOF Operator
SIZEOF Operator

## Slide 77: OFFSET Operator
OFFSET returns the offset of the data label, it represents the distance in bytes, of a label from the beginning of its enclosing segment
  Protected mode: 32 bits
  Real mode: 16 bits
The Protected-mode programs we use only a single segment (flat memory model).

## Slide 78: OFFSET: Examples
.data
bVal BYTE ?
wVal WORD ?
dVal DWORD ?
dVal2 DWORD ?
.code
mov esi,OFFSET bVal ; ESI = 00404000
mov esi,OFFSET wVal ; ESI = 00404001
mov esi,OFFSET dVal ; ESI = 00404003
mov esi,OFFSET dVal2 ; ESI = 00404007
Let's assume that the data segment begins at 00404000h:
data segment
bVal
wVal
dVal
…..
1 Byte
2 Bytes
4 Bytes
00404000h
This is a memory address
not a memory value
Notes: Sec06, Mar01

## Slide 79: OFFSET: Examples
OFFSET can also be applied to a direct-offset operand
Suppose myArray contains five 16-bit words
The following MOV instruction
  Obtains the offset of myArray,
  Adds 4,
  Moves the resulting address to ESI.
  We can say that ESI points to the third integer in the array:
.data
myArray WORD 1,2,3,4,5
.code
mov esi,OFFSET myArray + 4
ESI = 00404000 + 4
Notes: Sep28,TH 4pm
Sec03, 09 Mar 2

## Slide 80: OFFSET: Relating to C/C++
// C++ version:
char array[1000];
char * p = array;
The value returned by OFFSET is a pointer.
Compare the following code written for both C++ and assembly language:
; Assembly language:
.data
array BYTE 1000 DUP(?)
.code
mov esi,OFFSET array

## Slide 81: PTR Operator
Overrides the default type of a label (variable).
Provides the flexibility to access PART of a variable.
Used in combination with BYTE, SBYTE, WORD, SWORD, DWORD, SDWORD, FWORD, QWORD, or TBYTE
Ex. PTR operator makes it possible to move the low-order
Why wasn’t 1234h moved into AX?
But the WORD PTR operator makes it possible to move the low-order word (5678h) to AX:

## Slide 82: PTR Operator
Why wasn’t 1234h moved into AX?
x86 processors use the little endian storage format
low-order byte is stored at the variable’s starting address
For example, the doubleword 12345678h would be stored as:
When integers are loaded from memory into registers, the bytes are automatically re-reversed into their correct positions
(5678h)

## Slide 83: PTR Operator: Example1
.data
myDouble DWORD 12345678h
mov al,BYTE PTR myDouble ; AL = 78h
mov al,BYTE PTR [myDouble+1] ; AL = 56h
mov al,BYTE PTR [myDouble+2] ; AL = 34h
mov ax,WORD PTR myDouble ; AX = 5678h
mov ax,WORD PTR [myDouble+2] ; AX = 1234h
Memory Layout

## Slide 84: PTR Operator: Example2
PTR can also be used to combine elements of a smaller data type and move them into a larger operand.
.data
wordList WORD 5678h,1234h
.code
mov eax, DWORD PTR wordList
; EAX = 12345678h

## Slide 85: PTR Operator: Exercise
Use the following data definitions for Questions 6:
    myBytes BYTE 10h,20h,30h,40h
    myWords WORD 8Ah,3Bh,72h,44h,66h
    myDoubles DWORD 1,2,3,4,5
    myPointer DWORD myDoubles

## Slide 86: TYPE Operator
The TYPE operator returns the size, in bytes, of a single element of a data declaration.
.data
var1 BYTE ?
var2 WORD ?
var3 DWORD ?
var4 QWORD ?
.code
mov eax,TYPE var1 ; 1
mov eax,TYPE var2 ; 2
mov eax,TYPE var3 ; 4
mov eax,TYPE var4 ; 8

## Slide 87: LENGTHOF Operator
.data LENGTHOF
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 32
array2 WORD 5 DUP(3 DUP(?)) ; 15
array3 DWORD 1,2,3,4 ; 4
digitStr BYTE "12345678",0 ; 9
.code
mov ecx,LENGTHOF array1 ; 32
The LENGTHOF operator counts the number of elements in a single data declaration.

## Slide 88: SIZEOF Operator
.data SIZEOF
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 64
array2 WORD 5 DUP(3 DUP(?)) ; 30
array3 DWORD 1,2,3,4 ; 16
digitStr BYTE "12345678",0 ; 9
.code
mov ecx,SIZEOF array1 ; 64
The SIZEOF operator returns a value that is equivalent to multiplying LENGTHOF by TYPE.

## Slide 89: Outline
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions
Notes: Jun.29th, Summer2017

## Slide 90: Indirect Addressing
Indirect Operands
  Array Sum Example
Indexed Operands
Pointers
Notes: Mon 3pm, Oct 2,2017
TU 9:30, Oct 3

## Slide 91: Indirect Addressing (1)
Direct addressing becomes infeasible for array access.
Mov eax, arrayD
Mov eax, [arrayD+4]
Mov eax, [arrayD+8]
There is no way to parameterize the constant offset (e.g. 4)

## Slide 92: Indirect Addressing (2)
Indirect addressing can solve the issue
Consider the example.
  .data
  Val1 BYTE 11h, 33h, 55h
Store the address of the array in any 32-bit register.
  mov esi, OFFSET val1
The put that register inside the bracket to dereference it.
  mov al, [esi]
  Now Al contains 11h

## Slide 93: Indirect Addressing
Main memory
  mov esi,OFFSET arrayW
  .data
  arrayW WORD 1122h, 3344h, 5566h
  mov ax, [esi]
22
11
44
33
66
55
40440000
40440001
40440003
40440002
40440004
40440005
AX
ESI
22
11
4044000
  add esi, 2
  mov ax, [esi]
4044000+2 = 4044002
33
44

## Slide 94: Attendance

## Slide 95: Indirect Addressing: Indirect Operands
.data
val1 BYTE 10h,20h,30h
.code
mov esi,OFFSET val1
mov al,[esi] ; dereference ESI (AL = 10h)
inc esi
mov al,[esi] ; AL = 20h
inc esi
mov al,[esi] ; AL = 30h
An indirect operand holds the address of a variable, usually an array or string.
It can be dereferenced (just like a pointer).
🤔

## Slide 96: Indirect Addressing: Indirect Operands
.data
myCount WORD 7,3,2
.code
mov esi,OFFSET myCount
inc [esi] ; error: ambiguous
inc WORD PTR [esi] ; ok
Use PTR to clarify the size attribute of a memory operand.
The size of an operand may not be evident from the context of an instruction.

## Slide 97: Indirect Addressing: Array Sum Example
.data
arrayW WORD 1000h,2000h,3000h
.code
  mov esi,OFFSET arrayW
  mov ax,[esi]
  add esi,2 ; or: add esi,TYPE arrayW
  add ax,[esi]
  add esi,2
  add ax,[esi] ; AX = sum of the array
Indirect operands are ideal for traversing an array.
Note that the register in brackets must be incremented by a value that matches the array type.
ToDo: Modify this example for an array of doublewords.

## Slide 98: Indirect Addressing
Indirect Operands
  Array Sum Example
Indexed Operands
Pointers

## Slide 99: Indexed Operands
Instead of storing the address in ESI register (or any 32-bit register)
  You can use these registers as counter.
An indexed operand adds a constant to a register to generate an effective address.
There are two notational forms:
[label + reg] label[reg]
[var1 + esi] OR var1[esi]

## Slide 100: Indexed Operands
.data
arrayW WORD 1000h,2000h,3000h
.code
mov esi,0
mov ax,[arrayW + esi] ; AX = 1000h
mov ax,arrayW[esi] ; alternate format
add esi,2
add ax,[arrayW + esi]
etc.
An indexed operand adds a constant to a register to generate an effective address.
There are two notational forms:
[label + reg] label[reg]
ToDo: Modify this example for an array of doublewords.

## Slide 101: Indirect Addressing
Indirect Operands
Array Sum Example
Indexed Operands
Pointers

## Slide 102: Pointers
.data
arrayW WORD 1000h,2000h,3000h
myptrW arrayW
.code
mov esi,myptrW
mov ax,[esi] ; AX = 1000h
You can declare a pointer variable that contains the offset of another variable.
Alternate format:
myptrW DWORD OFFSET arrayW
DWORD

## Slide 103: Outline
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions
Notes: Sec06, Mar6
Sec03, Mar7
Sec03, Mar9

## Slide 104: JMP and LOOP Instructions
JMP Instruction
LOOP Instruction
  LOOP Example
Summing an Integer Array
Copying a String

## Slide 105: JMP and LOOP Instructions
CPU loads and executes programs sequentially
Current instruction might be a one that transfer control to a different memory address
Assembly language programs use conditional instructions to implement high-level statements
  IF statements and Loops.
offset machine code source code
00000000 B8 00000000 mov eax,0 00000005 EB 03 jmp addone 00000007 83 C0 02 add eax,2
0000000A addone: 0000000A 40 inc eax
0000000B 83 C0 01 add eax,4294967295

## Slide 106: JMP and LOOP Instructions
There are two basic types of transfers:
  Unconditional Transfer
  Conditional Transfer
Unconditional Transfer: Control is transferred to a new location in all cases
  New address is loaded into the instruction pointer, EIP,
    causing execution to continue at the new address.
  The JMP instruction does this.

## Slide 107: JMP Instruction (Unconditional Transfer)
JMP is an unconditional jump to a label that is usually within the same procedure.
Syntax: JMP target
Logic: EIP  target
offset machine code source code
00000005 EB 03 jmp addone 00000007 83 C0 02 add eax,2
0000000A addone: 0000000A 40 inc eax
EIP=
EIP=

## Slide 108: JMP Instruction (Unconditional Transfer)
JMP is an unconditional jump to a label that is usually within the same procedure.
Example:
A jump outside the current procedure must be to a special type of label called a global label (see Section 5.5.2.3 for details).
mov eax,0
Jmp addone
add eax,2
addone:
inc eax
add eax, 4294967295 ;2^32 = 4294967296
Try Visual Studio

## Slide 110: LOOP Instruction (Conditional Transfer)
Conditional Transfer: The program branches if a certain condition is true
  A wide variety of conditional transfer instructions can be combined to create conditional logic structures.
The LOOP instruction creates a counting loop
Syntax: LOOP target
Logic:
  ECX  ECX – 1
  if ECX != 0, jump to target
The CPU interprets true/false conditions based on
the contents of the ECX and Flags registers.

## Slide 111: LOOP: Example
The following loop calculates the sum of the integers 5 + 4 + 3 +2 + 1:
mov ax,0
mov ecx,5
L1: add ax,cx
loop L1
Logic: ECX  ECX – 1
if ECX != 0, jump to target
00000000 66 B8 0000 mov ax,0
00000004 B9 00000005 mov ecx,5
00000009 66 03 C1 L1: add ax,cx
0000000C E2 FB loop L1
0000000E
offset machine code source code
How assembler calculates FB?
Notes: Tu, Oct 3,2017, 4pm

## Slide 113: LOOP: Example (Conditional Transfer)
The assembler calculates the distance, in bytes, between
  the offset of the following instruction and
  the offset of the target label.
00000009 66 03 C1 L1: add ax,cx
0000000C E2 FB loop L1
0000000E
offset machine code source code

## Slide 114: LOOP: Example (Conditional Transfer)
When LOOP is assembled,
  The current location = 0000000E (offset of the next instruction)
  Distance is
    -5 (FBh)
    FBh is added to the the current location,
    causing a jump to location 00000009:
  Target Label location address = Offset of the next instruction + Distance
  00000009  0000000E + FB
  The relative offset is added to EIP = 00000009

## Slide 115: LOOP: Example
If the relative offset is encoded in a single signed byte,
(a) what is the largest possible backward jump?
(b) what is the largest possible forward jump?
-128
+127

## Slide 116: LOOP: Example
What will be the final value of AX?
mov ax,6
mov ecx,4
L1:
inc ax
loop L1
How many times will the loop execute?
mov ecx,0
X2:
inc ax
loop X2
10
A common programming error is to inadvertently initialize ECX to zero before beginning a loop.

## Slide 117: LOOP: Nested LOOP

## Slide 118: LOOP: Nested LOOP
If you need to code a loop within a loop, you must save the outer loop counter's ECX value.
In the following example, the outer loop executes 3 times, and the inner loop 2 times.
.data
count DWORD ?
.code
mov ecx,3 ; set outer loop count
L1:
mov count,ecx ; save outer loop count
mov ecx,2 ; set inner loop count
L2: .
  .
  loop L2 ; repeat the inner loop
mov ecx,count ; restore outer loop count
loop L1 ; repeat the outer loop

## Slide 119: JMP and LOOP Instructions
JMP Instruction
LOOP Instruction
  LOOP Example
Summing an Integer Array
Copying a String

## Slide 120: Array: Summing an Integer Array
.data
intarray WORD 100h,200h,300h,400h
.code
  mov edi,OFFSET intarray ; address of intarray
  mov ecx,LENGTHOF intarray ; loop counter
  mov ax,0 ; zero the accumulator
L1:
  add ax,[edi] ; add an integer
  add edi,TYPE intarray ; point to next integer
loop L1 ; repeat until ECX = 0
The following code calculates the sum of an array of 16-bit integers.
1. Assign the array’s address to a register that will serve as an indexed operand.
2. Initialize the loop counter to the length of the array.
3. Assign zero to the register that accumulates the sum.
4. Create a label to mark the beginning of the loop.
5. In the loop body, add a single array element to the sum.
6. Point to the next array element.
7. Use a LOOP instruction to repeat the loop.
1
2
3
4
5
6
7
Notes: The SIZEOF operator returns a value that is equivalent to multiplying LENGTHOF by TYPE.

## Slide 121: Array: Summing an Integer Array
What changes would you make to the program on the previous slide if you were summing a doubleword array?
mov ax,0
add ax,[edi]
intarray WORD 100h,200h,300h,400h

## Slide 122: JMP and LOOP Instructions
JMP Instruction
LOOP Instruction
  LOOP Example
Summing an Integer Array
Copying a String

## Slide 123: Copying a String
Use a loop to copy a string, represented as an array of bytes with a null terminator value.
source BYTE "This is the source string",0
target BYTE SIZEOF source DUP(0)
The target string must have enough available space to receive the copied characters, including the null byte at the end 🤔:
Indexed addressing works well for this type of operation because the same index register references both strings.
mov esi,0 ; index register
mov al,source[esi] ; get char from source
mov target[esi],al
The SIZEOF operator returns a value that is equivalent to multiplying LENGTHOF by TYPE.
Notes: The SIZEOF operator returns a value that is equivalent to multiplying LENGTHOF by TYPE.
26

## Slide 124: Copying a String
.data
source BYTE "This is the source string",0
target BYTE SIZEOF source DUP(0)
.code
mov esi,0 ; index register
mov ecx,SIZEOF source ; loop counter
L1:
mov al,source[esi] ; get char from source
mov target[esi],al ; store it in the target
inc esi ; move to next character
loop L1 ; repeat for entire string
good use of SIZEOF
The following code copies a string from source to target:

## Slide 126: Copying a String
Rewrite the program shown in the previous slide, using indirect addressing rather than indexed addressing.

## Slide 127: Summary
Data Transfer
  MOV – data transfer from source to destination
  MOVSX, MOVZX, XCHG
Operand types
  direct, direct-offset, indirect, indexed
Arithmetic
  INC, DEC, ADD, SUB, NEG
  Sign, Carry, Zero, Overflow flags
Operators
  OFFSET, PTR, TYPE, LENGTHOF, SIZEOF, TYPEDEF
JMP and LOOP – branching instructions