## Slide 1: CSC 3210 Computer Organization and Programming
Chapter 6: Conditional Processing
if A > B ...
while X > 0 and X < 200 ...
if check_for_error( N ) = true
Notes: An operator is a symbol that tells the compiler to perform specific mathematical or logical functions.
C language built-in operators
- Arithmetic Operators
- Relational Operators
- Logical Operators
- Bitwise Operators
- Assignment Operators

## Slide 2: Outline
Boolean and Comparison Instructions
Conditional Jumps
Conditional Structures
Conditional Control Flow Directives

## Slide 3: Boolean and Comparison Instructions
CPU Status Flags
AND Instruction
OR Instruction
XOR Instruction
NOT Instruction
  Applications
TEST Instruction
CMP Instruction
Boolean operations are the core of all decision statements because they affect the CPU status flags.
if A > B ...
while X > 0 and X < 200 ...
if check_for_error( N ) = true

## Slide 4: Status Flags - Review
Boolean instructions affect the Zero, Carry, Sign, Overflow, and Parity flags.

## Slide 5: Status Flags - Review
The Zero flag is set when the result of an operation equals zero.
The Carry flag is set when an instruction generates a result that is too large (or too small) for the destination operand.
The Sign flag is set if the destination operand is negative, and it is clear if the destination operand is positive.
The Overflow flag is set when an instruction generates an invalid signed result.
The Parity flag is set when an instruction generates an even number of 1 bits in the low byte of the destination operand.

## Slide 6: AND Instruction
Performs a Boolean AND operation between each pair of matching bits in two operands
Syntax:
AND
AND destination, source (same operand types as MOV)

## Slide 7: AND Instruction
Flags
  The AND instruction always clears the Overflow and Carry flags.
  It modifies the Sign, Zero, and Parity flags
    Consistent with the value assigned to the destination operand.
Example:
  Suppose the following instruction results in a value of Zero in the al register.
  Thus, the Zero flag will be set:
and al,1Fh

## Slide 8: AND Example
mov ax,wordVal
And ax,1 ; low bit set?
jz EvenValue ; jump if Zero flag set
Task: Jump to a label if an integer is even.
Solution: AND the lowest bit with a 1,
If the result is Zero, the number was even.
JZ (jump if Zero) is covered in Section 6.3.

## Slide 9: OR Instruction
Performs a Boolean OR operation between each pair of matching bits in two operands
Syntax: OR destination, source
OR

## Slide 10: OR Instruction
Flags
  The OR instruction always clears the Carry and Overflow flags.
  It modifies the Sign, Zero, and Parity flags
    consistent with the value assigned to the destination operand.
  Example: OR a number with itself (or zero) to obtain certain information about its value:
or al,al

## Slide 11: OR Instruction
The values of the Zero and Sign flags indicate the following about the contents of AL:

## Slide 12: OR Example
or al,al
jnz IsNotZero ; jump if not zero
Task: Jump to a label if the value in AL is not zero.
Solution: OR the byte with itself, then use the JNZ (jump if not zero) instruction.
ORing any number with itself does not change its value.

## Slide 13: XOR Instruction
Performs a Boolean exclusive-OR operation between each pair of matching bits in two operands
Syntax: XOR destination, source
XOR
XOR is a useful way to toggle (invert) the bits in an operand.

## Slide 14: XOR Instruction
XOR
XOR is a useful way to toggle (invert) the bits in an operand.
Example:
  bit masking:
    A bit exclusive-ORed with 0 retains its value,
    A bit exclusive-ORed with 1 is toggle (complemented).

## Slide 15: XOR Instruction
Flags
  The XOR instruction always clears the Overflow and Carry flags.
  XOR modifies the Sign, Zero and Parity flags
    consistent with the value assigned to the destination operand.
Example:
An effective way to check the parity of a number without changing its value is to exclusive-OR the number with zero:
The Parity flag (PF) is set when The least significant byte of the destination has an even number of 1 bits.
Notes: Thursday, 06, Jully.

## Slide 16: XOR Instruction : Another Property

## Slide 17: XOR Application: Encrypting a String
KEY = 239 ; can be any byte value between 1-255
BUFMAX = 128
.data
buffer BYTE BUFMAX+1 DUP(0)
bufSize DWORD BUFMAX
.code
  mov ecx,bufSize ; loop counter
  mov esi,0 ; index 0 in buffer
L1:
  xor buffer[esi],KEY ; translate a byte
  inc esi ; point to next byte
  loop L1
The following loop uses the XOR instruction to transform every character in a string into a new value.
Enter the plain text: Attack at dawn.
Cipher text: «¢¢Äîä-Ä¢-ïÄÿü-Gs
Decrypted: Attack at dawn.

## Slide 18: XOR Application: Encrypting a String
Tasks:
  Input a message (string) from the user
  Encrypt the message
  Display the encrypted message
  Decrypt the message
  Display the decrypted message
View the Encrypt.asm program's source code. Sample output:
Enter the plain text: Attack at dawn.
Cipher text: «¢¢Äîä-Ä¢-ïÄÿü-Gs
Decrypted: Attack at dawn.

## Slide 19: NOT Instruction
Performs a Boolean NOT operation on a single destination operand
Syntax: NOT destination
NOT
Flags
  No flags are affected by the NOT instruction.

## Slide 20: TEST Instruction
Performs a nondestructive AND operation between each pair of matching bits in two operands
No operands are modified
Sets the Sign, Zero, and Parity flags based on the value assigned to the destination operand.
test al,00000011b
jnz ValueFound
ZF = ?
Example 1: jump to a label if either bit 0 or bit 1 in AL is set.
Notes: Tus, Oct 10, 2017

## Slide 21: CMP Instruction
Compares the destination operand to the source operand (HOW 🤔)
  CMP performs implied subtraction of source operand from destination operand
  Nondestructive subtraction of source from destination (destination operand is not changed)
Syntax:
The most common boolean expressions involve some type of comparison:
if A > B ...
while X > 0 and X < 200 ...
if check_for_error( N ) = true
CMP instruction is used to compare integers (signed and unsigned)
CMP destination, source
🗝
Notes: Wed, Oct-11,3pm

## Slide 22: CMP Instruction (unsigned )
Flags
  The CMP instruction changes the Overflow, Sign, Zero, Carry, Auxiliary Carry, and Parity flags
    According to the value the destination operand would have had if actual subtraction had taken place.
When two unsigned operands are compared,
  Zero and Carry flags indicate the following relations between operands:
Why CF is 1?

## Slide 23: CMP Instruction (signed )
Flags
2) When two signed operands are compared,
  the Sign, Zero, and Overflow flags indicate the following relations between operands:

## Slide 24: CMP Instruction (unsigned integers)
Example1: destination == source
mov al,5
cmp al,5 ; Zero flag set
Example2: destination < source
mov al,4
cmp al,5 ; Carry flag set
The comparisons shown here are performed with unsigned integers.
😳

## Slide 25: CMP Instruction (unsigned integers)
Example3: destination > source
mov al,6
cmp al,5 ; ZF = 0, CF = 0
(both the Zero and Carry flags are clear)

## Slide 26: CMP Instruction (signed integers)
Example1: destination > source
mov al,5
cmp al,-2 ; Sign flag == Overflow flag
The comparisons shown here are performed with signed integers
Example2: destination < source
mov al,-1
cmp al,5 ; Sign flag != Overflow flag
😳

## Slide 27: Outline
Boolean and Comparison Instructions
Conditional Jumps
Conditional Structures
Conditional Control Flow Directives
Implement high-level logic structures using a combination of
comparisons and jumps.
if A > B ...
while X > 0 and X < 200 ...
cmp eax,0
jz L1 ; jump if ZF = 1
Notes: Oct12-TH,4pm

## Slide 29: Conditional Jumps
Jumps Based On . . .
  Specific flags
  Equality
  Unsigned comparisons
  Signed Comparisons
Applications
Search of an Array
First, an operation such as CMP, AND, or SUB modifies the CPU status flags.
Second, a conditional jump instruction tests the flags and causes a branch to a new address.
Compare and then Jump
🗝

## Slide 30: Jcond Instruction
A conditional jump instruction branches to a label
  When specific status flag condition is true
Syntax
Jcond destination
cond refers to a flag condition identifying the state of one or more flags.
The following examples are based on the Carry and Zero flags:
CPU status flags are most commonly set by
arithmetic, comparison, and boolean instructions.

## Slide 31: Conditional Jumps (Example1)
First, an operation such as CMP, AND, or SUB modifies the CPU status flags.
Second, a conditional jump instruction tests the flags and causes a branch to a new address.
Compare and then Jump or NOT
🗝
- The CMP instruction compares EAX to Zero.
The JZ (Jump if zero) instruction jumps to label L1 if the Zero flag was set by the CMP instruction:
cmp eax,0
jz L1 ; jump if ZF = 1
.
.
L1:
.
.

## Slide 32: Conditional Jumps (Example2)
First, an operation such as CMP, AND, or SUB modifies the CPU status flags.
Second, a conditional jump instruction tests the flags and causes a branch to a new address.
Compare and then Jump
🗝
The AND instruction performs a bitwise AND on the DL register, affecting the Zero flag.
The JNZ (jump if not Zero) instruction jumps if the Zero flag is clear:
and dl,10110000b
jnz L2 ; jump if ZF = 0
.
.
L2:

## Slide 33: Types of Conditional Jumps Instructions
The conditional jump instructions can be divided into four groups:
  Jumps based on specific flag values
  Jumps based on equality between operands or the value of (E)CX
  Jumps based on comparisons of unsigned operands
  Jumps based on comparisons of signed operands
Conditional jump instructions are able to
  Compare signed and unsigned integers and
    Perform actions based on the values of individual CPU flags.

## Slide 34: Jumps Based on Specific Flags

## Slide 35: Jumps Based on Equality
CMP leftOp, rightOp

## Slide 36: Jumps Based on Unsigned Comparisons
A and B
CMP leftOp, rightOp

## Slide 37: Jumps Based on Signed Comparisons
G and L
CMP leftOp, rightOp

## Slide 38: Conditional Jumps
Jumps Based On . . .
  Specific flags
  Equality
  Unsigned comparisons
  Signed Comparisons
Applications
Search of an Array

## Slide 39: Applications 1
cmp eax,ebx
ja Larger ;jump if above
Task: Jump to a label if unsigned EAX is greater than EBX
Solution: Use CMP, followed by JA
cmp eax,ebx
jg Greater ; jump if greater
Task: Jump to a label if signed EAX is greater than EBX
Solution: Use CMP, followed by JG
A and B
G and L

## Slide 40: Applications 2
cmp eax,Val1
jbe L1 ; below or equal
Jump to label L1 if unsigned EAX is less than or equal to Val1
cmp eax,Val1
jle L1
Jump to label L1 if signed EAX is less than or equal to Val1
A and B
G and L

## Slide 41: Applications 3
  mov Large,bx
  cmp ax,bx
  jna Next
  mov Large,ax
Next:
Compare unsigned AX to BX, and copy the larger of the two into a variable named Large
  mov Small,ax
  cmp bx,ax
  jnl Next
  mov Small,bx
Next:
Compare signed AX to BX, and copy the smaller of the two into a variable named Small
A and B
G and L

## Slide 42: Applications 4
  cmp WORD PTR [esi],0
  je L1
Jump to label L1 if the memory word pointed to by ESI equals Zero
test DWORD PTR [edi],1
jz L2
Jump to label L2 if the doubleword in memory pointed to by EDI is even

## Slide 43: Applications 5
and al,00001011b ; clear unwanted bits
cmp al,00001011b ; check remaining bits
je L1 ; all set? jump to L1
Task: Jump to label L1 if bits 0, 1, and 3 in AL are all set.
Solution: 1. Clear all bits except bits 0, 1,and 3.
2. Then compare the result with 00001011 binary.

## Slide 44: Conditional Jumps
Jumps Based On . . .
  Specific flags
  Equality
  Unsigned comparisons
  Signed Comparisons
Applications
Search of an Array

## Slide 45: Search of an Array
A common programming task is to search for values in an array that meet some criteria
Example:
  The following program looks for the first nonzero value in an array of 16-bit integers
    If it finds one, it displays the value
    Otherwise, it displays a message stating that a nonzero value was not found

## Slide 47
Crlf:
Writes an end-of-line sequence to the console window.
WriteString Writes a null-terminated string to the console window.
WriteInt
Writes a signed 32-bit integer to the console window in decimal format.
Why use ebx and not esi?
Notes: Mon, Oct,16,3pm

## Slide 48: Outline
Boolean and Comparison Instructions
Conditional Jumps
Conditional Structures
Conditional Control Flow Directives

## Slide 49: Conditional Structures
Block-Structured IF Statements
  Compound Expressions with AND
  Compound Expressions with OR
WHILE Loops
Notes: Oct-17-Tu,9:30

## Slide 50: Conditional Structures
A conditional structure is defined to be one or more conditional expressions
Those conditional expressions trigger a choice between different logical branches
Each branch causes a different sequence of instructions to execute.
When the condition is true, execute the body
When the condition is false, don't execute the body, jump over it.

## Slide 51: Block-Structured IF Statements
An IF structure imply that a boolean expression is followed by one or two lists of statements:
Two types:
  1. IF-Then
    Statement/s performed when the expression is true
    Next statement/s performed when the expression is false:
.
.
.

## Slide 52: Block-Structured IF Statements
The else part is optional.
  2. IF-Then-Else
    Statement/s performed when the expression is true
    Another performed when the expression is false:

## Slide 53: Block-Structured IF Statements
IF statement is translated into assembly language with a
  CMP instruction followed by
  Conditional jumps.
When op1 or op2 is a memory operand (a variable),
  One of them must be moved to a register before executing CMP.

## Slide 54: Block-Structured IF Statements
If ( AX > 10){
//if block code
}
else{
//else block code
}

## Slide 55: Block-Structured IF Statements
CMP AX, 10
Jump (conditional) to ELSE if (AX>10) is FALSE
// if block code
Label:
  // ELSE block code
If ( AX > 10){
//if block code
}
else{
//else block code
}

## Slide 56: Block-Structured IF Statements
CMP AX, 10
Jump (conditional) to ELSE if (AX>10) is FALSE
// if block code
Label:
  // ELSE block code
If ( AX > 10){
//if block code
}
else{
//else block code
}
Problem! : Conditional Jumps trigger when CONDITION is TRUE!

## Slide 57: Block-Structured IF Statements
CMP AX, 10
Jump (conditional) to ELSE if (AX>10) is FALSE
// if block code
Label:
  // ELSE block code
If ( AX > 10){
//if block code
}
else{
//else block code
}
Solution : Negate the condition
Now, it can jump when condition is TRUE.

## Slide 58: Block-Structured IF Statements
When the condition is true, execute the body
When the condition is false, don't execute the body, jump over it.
This is the jump case
Thus, jump when the condition is false.
🗝
- x86 Jump instructions jump
when the condition is true
- Thus, we often need to reverse the condition.
2
1

## Slide 59: Block-Structured IF Statements
How to reverse a condition?
  Using DeMorgan's Law
  In order to branch on a negated condition, we need to know the negation of various conditions
Condition | Negated Condition
x > y | x <= y
x >= y | x < y
x < y | x >= y
x <= y | x > y
= | !=
<cond1> && <cond1> | ! <cond1> ¦¦ ! <cond2>
<cond1> ¦¦ <cond1> | ! <cond1> && ! <cond2>

## Slide 60: IF Statements: Example1 (IF-Then)
Implement the following pseudocode in assembly language.
All values are unsigned:
if( ebx <= ecx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)
Reverse The IF Condition
IF statement is translated into assembly language with a
  CMP instruction followed by
  Conditional jumps.
If op1 or op2 is a memory operand (a variable):
  one of them must be moved to a register before executing CMP.

## Slide 61: IF Statements: Example1 (IF-Then)
Implement the following pseudocode in assembly language.
All values are unsigned:
  cmp ebx,ecx
  ja next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)
A and B
Reverse The IF Condition
IF statement is translated into assembly language with a
  CMP instruction followed by
  Conditional jumps.
If op1 or op2 is a memory operand (a variable):
  one of them must be moved to a register before executing CMP.

## Slide 63: IF Statements: Example2 (IF-Then-Else)
if( op1 == op2 )
X = 1;
else
X = 2;
Reverse The IF Condition
Implement the following pseudocode in assembly language.
IF statement is translated into assembly language with a
  CMP instruction followed by
  Conditional jumps.
If op1 or op2 is a memory operand (a variable):
  one of them must be moved to a register before executing CMP.
Notes: Sec03 Mar 28th

## Slide 64: IF Statements: Example2 (IF-Then-Else)
  mov eax,op1
  cmp eax,op2
  jne L1
  mov X,1
  jmp L2
L1: mov X,2
L2:
if( op1 == op2 )
X = 1;
else
X = 2;
Reverse The IF Condition
Implement the following pseudocode in assembly language.
IF statement is translated into assembly language with a
  CMP instruction followed by
  Conditional jumps.
If op1 or op2 is a memory operand (a variable):
  one of them must be moved to a register before executing CMP.
Notes: Sec03 Mar 28th

## Slide 65: IF Statements: Example3 (IF-Then-Else)
Implement the following pseudocode in assembly language.
All values are 32-bit signed integers:
if( var1 <= var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}
(There are multiple correct solutions to this problem.)
Do not Reverse the Condition
IF statement is translated into assembly language with a
  CMP instruction followed by
  Conditional jumps.
If op1 or op2 is a memory operand (a variable):
  one of them must be moved to a register before executing CMP.

## Slide 66: IF Statements: Example3 (IF-Then-Else)
Implement the following pseudocode in assembly language.
All values are 32-bit signed integers:
if( var1 <= var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}
(There are multiple correct solutions to this problem.)
Do not Reverse the Condition
IF statement is translated into assembly language with a
  CMP instruction followed by
  Conditional jumps.
If op1 or op2 is a memory operand (a variable):
  one of them must be moved to a register before executing CMP.
  1. Compare two operands
  2. If condition TRUE
  jump to IF BLOCK
  3. ELSE Block
  4. Jump over IF block
  5. IF block

## Slide 67: IF Statements: Example3 (IF-Then-Else)
Implement the following pseudocode in assembly language.
All values are 32-bit signed integers:
  mov eax,var1
  cmp eax,var2
  jle L1
  mov var3,6
  mov var4,7
  jmp L2
L1: mov var3,10
L2:
if( var1 <= var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}
(There are multiple correct solutions to this problem.)
G and L
Do not Reverse the Condition
IF statement is translated into assembly language with a
  CMP instruction followed by
  Conditional jumps.
If op1 or op2 is a memory operand (a variable):
  one of them must be moved to a register before executing CMP.

## Slide 68: Conditional Structures
Block-Structured IF Statements
  Compound Expressions with AND
  Compound Expressions with OR
WHILE Loops
Notes: Sec06 Mar 27th
Sec09 Mar 28th

## Slide 69: Attendance

## Slide 70: Compound Expression with AND (Example1)
if (al > bl) AND (bl > cl)
X = 1;

## Slide 71: Compound Expression with AND (Example1)
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is false, the second expression is skipped:
if (al > bl) AND (bl > cl)
X = 1;
cmp al,bl ; first expression...
ja L1
jmp next
L1:
cmp bl,cl ; second expression...
ja L2
jmp next
L2: ; both are true
mov X,1 ; set X to 1
next: …
A and B
Do not Reverse

## Slide 72: Compound Expression with AND (Example1)
if (al > bl) AND (bl > cl)
X = 1;
Reverse The IF Condition

## Slide 73: Compound Expression with AND (Example2)
cmp al,bl ; first expression...
jbe next ; quit if false
cmp bl,cl ; second expression...
jbe next ; quit if false
mov X,1 ; both are true
next:
.
.
if (al > bl) AND (bl > cl)
X = 1;
But the following implementation uses 29% less code by reversing the first relational operator.
We allow the program to "fall through" to the second expression:
Reverse The IF Condition

## Slide 74
cmp al,bl ; first expression...
jbe next ; quit if false
cmp bl,cl ; second expression...
jbe next ; quit if false
mov X,1 ; both are true
next:
if (al > bl) AND (bl > cl)
X = 1;
cmp al,bl ; first expression...
ja L1
jmp next
L1:
cmp bl,cl ; second expression...
ja L2
jmp next
L2: ; both are true
mov X,1 ; set X to 1
next:
Method 1
Method 2
Do not Reverse the Condition
Reverse the Condition

## Slide 75: Compound Expression with AND (Example3)
Implement the following pseudocode in assembly language.
All values are unsigned:
  cmp ebx,ecx
  ja next
  cmp ecx,edx
  jbe next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx
&& ecx > edx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)
Reverse The IF Condition

## Slide 76: Conditional Structures
Block-Structured IF Statements
  Compound Expressions with AND
  Compound Expressions with OR
WHILE Loops

## Slide 77: Compound Expression with OR
if (al > bl) OR (bl > cl)
X = 1;
Reverse the second Condition

## Slide 79: Compound Expression with OR
if (al > bl) OR (bl > cl)
X = 1;
cmp al,bl ; is AL > BL?
ja L1 ; yes
cmp bl,cl ; no: is BL > CL?
jbe next ; no: skip next statement
L1: mov X,1 ; set X to 1
next:
In the following implementation, the code branches to L1
  if the first expression is true
  otherwise, it falls through to the second CMP instruction.
The second expression reverses the > operator and uses JBE instead:
Reverse the second Condition

## Slide 80: Conditional Structures
Block-Structured IF Statements
  Compound Expressions with AND
  Compound Expressions with OR
WHILE Loops

## Slide 81: WHILE Loops
A WHILE loop tests a condition first before performing a block of statements.
As long as the loop condition remains true, the statements are repeated.
When implementing this structure in assembly language,
  it is convenient to reverse the loop condition
  and jump to endwhile if a condition becomes true

## Slide 84: WHILE Loops: Example1
G and L
Reverse The loop Condition
Notes: Verify this: jnl and jnle
Tu, Oct, 17, 4pm

## Slide 85: WHILE Loops: Example1
mov eax,val1 ; copy variable to EAX?
beginwhile:
cmp eax,val2 ; if not (val1 < val2)
jge endwhile ; exit the loop
inc eax ; val1++;
dec val2 ; val2--;
jmp beginwhile ; repeat the loop
endwhile:
mov val1,eax ; save new value for val1
G and L
Reverse The loop Condition
Notes: Verify this: jnl and jnle
Tu, Oct, 17, 4pm

## Slide 87: WHILE Loops: Example2
while( eax < ebx)
eax = eax + 1;
top:
cmp eax,ebx ; check loop condition
jae next ; false? exit loop
inc eax ; body of loop
jmp top ; repeat the loop
next:
This is a possible implementation
A and B
Reverse The loop Condition

## Slide 88: WHILE Loops: Example3
top: cmp ebx,val1 ; check loop condition
ja next ; false? exit loop
add ebx,5 ; body of loop
dec val1
jmp top ; repeat the loop
next:
while( ebx <= val1)
{
ebx = ebx + 5;
val1 = val1 - 1
}
Implement the following loop, using unsigned 32-bit integers:
A and B
Reverse The loop Condition

## Slide 89: WHILE Loops: Example 4
IF statement Nested in a Loop
Calculates the sum of all
array elements greater than the value in sample (50)

## Slide 90: WHILE Loops: Example 4
IF statement Nested in a Loop

## Slide 91: WHILE Loops: Example 4
IF statement Nested in a Loop
Loop
IF
😳
40/4 = 10

## Slide 92: Outline
Boolean and Comparison Instructions
Conditional Jumps
Conditional Structures
Application: Finite-State Machines See the book
Conditional Control Flow Directives See the book

## Slide 93: Summary
Bitwise instructions (AND, OR, XOR, NOT, TEST)
  manipulate individual bits in operands
CMP – compares operands using implied subtraction
  sets condition flags
Conditional Jumps & Loops
  equality: JE, JNE
  flag values: JC, JZ, JNC, JP, ...
  signed: JG, JL, JNG, ...
  unsigned: JA, JB, JNA, ...
  LOOPZ, LOOPNZ, LOOPE, LOOPNE (Just know them)
Conditional Structures
  IF statement
  While loop