## Slide 1: CSC 3210 Computer Organization and Programming
Dr. Zulkar Nine
mnine@gsu.edu
Georgia State University
Spring 2021
Chapter 2: x86 Processor
Architecture

## Slide 2: X86 Processor Architecture
One step before using assembly language
  What is the selected processor Internal architecture and capabilities.
What is the underline hardware associated with X86?
Assembly language is a great tool for learning how a computer works.
  It require you to have working knowledge of computer hardware
You should have some basic knowledge about the processor and the system architecture in order to effectively program in the assembly language.

## Slide 3: Outline
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 4: General Concepts
Basic microcomputer design
Instruction execution cycle
Reading from memory
How programs run

## Slide 5: General Concepts: Basic Microcomputer Design
ALU performs arithmetic and logical (bitwise) operations
Control unit (CU) coordinates sequence of execution steps
Clock synchronizes CPU operations with other system components
Central Processing Unit (CPU)
Register
ALU
CU
clock
Memory Storage Unit
I/O
Device
#1
I/O
Device
#1
Data bus
Control bus
Address bus

## Slide 6: General Concepts: Basic Microcomputer Design
A bus: a group of parallel wires that transfer data
  bus types:
    address
    data
    control

## Slide 7: General Concepts: Basic Microcomputer Design
The Address bus holds the addresses of instructions and data, when the currently executing instruction transfers data between the CPU and memory.
The Data bus transfers instructions and data between the CPU and memory.
The Control bus uses binary signals to synchronize actions of all devices attached to the system bus.

## Slide 8: General Concepts: Clock
The system clock provides a timing signal to synchronize the operations of the system.
  Synchronizes all CPU and BUS operations
A clock is a sequence of 1’s and 0’s
The frequency:
is the number of cycles that happens each second
Notes: TH, 9:30, Sep 31

## Slide 9: General Concepts: Clock
The clock frequency is measured in the number of cycles per second.
This number is referred to as Hertz (Hz: the unit of frequency, defined as one cycle per second).
  MHz and GHz represent 106 and 109 cycles per second
The system clock defines the speed at which the system operates.

## Slide 11: General Concepts: Clock
Ex: transfer of data from a memory location to X86 (Pentium) takes three clock cycles.
The clock period is defined as the length of time taken by one clock cycle .
If it takes three clock cycles to execute an instruction, it takes 3 X 1 ns = 3 ns.
Machine (clock) cycle measures time of a single operation
Clock is used to trigger events

## Slide 12: General Concepts: Clock
A machine instruction requires one clock cycle to execute, few require 50 clocks
Instructions require memory access: Empty clock cycle, wait states, Why?
  CPU, system bus, and memory circuits
Notes: Wed, 30th Aug

## Slide 13: Clock per Instruction (CPI)
Is an effective average.
It is the average number of clocks required by the instructions in a program.
In a program 60% instructions takes 4 clock cycles and the rest of the instructions takes 1 clock cycles.
CPI = 0.6 * 4 + 0.4 * 1 = 2.8 clocks per instruction.

## Slide 14: Million Instructions Per Second
Step 1: Perform Divide operation between no. of instructions and Execution time.
Step 2: Perform Divide operation between that variable and 1 million for finding millions of instructions per second.
For example,
  if a computer completed 2 million instructions in 0.10 seconds
  2 million/0.10 = 20 million.
  No of MISP=20 million/1 million
  =20