## Slide 1: CSC 3210 Computer Organization and Programming
Dr. Zulkar Nine
mnine@gsu.edu
Georgia State University
Spring 2021
Chapter 4: Data Transfers,
Addressing, and Arithmetic

## Slide 2: Outline
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions

## Slide 3: Data Transfer Instructions
Operand Types
Instruction Operand Notation
Direct Memory Operands
MOV Instruction
Zero & Sign Extension
XCHG Instruction
Direct-Offset Instructions

## Slide 4: Data Transfer Instructions: Operand Types
Immediate – a constant integer (8, 16, or 32 bits)
  value is encoded within the instruction
Register – the name of a register
  register name is converted to a number and encoded within the instruction
Memory – reference to a location in memory
  memory address is encoded within the instruction, or a register holds the address of a memory location
00000000 .data
00000000 00000000 sum DWORD 0
00000000 .code
00000000 main proc
00000000 B8 00000008 mov eax, 8 00000005 83 C0 04 add eax, 4 00000008 A3 00000000 R mov sum, eax
Listing File

## Slide 5: Data Transfer Instructions: Instruction Operand Notation
MOV reg,reg
MOV mem,reg
MOV reg,mem
MOV mem,imm
MOV reg,imm

## Slide 6: Data Transfer Instructions
Register to Register
Register to Memory , Vice versa
0011010
0011012
0011014

## Slide 7: How to see variables in VS

## Slide 8: Data Transfer Instructions: Direct Memory Operands
A direct memory operand is a named reference to storage in memory
.data
var1 BYTE 10h
.code
mov al,var1 ; AL = 10h
mov al,[var1] ; AL = 10h
alternate format

## Slide 9: Data Transfer Instructions: Direct Memory Operands
The named reference (label) is automatically dereferenced by the assembler
.data
var1 BYTE 10h
Suppose var1 were located at offset 10400h.
The following instruction copies its value into the AL register:
mov al, var1
It would be assembled into the following machine instruction:
A0 00010400

## Slide 10: Data Transfer Instructions: Direct Memory Operands
The named reference (label) is automatically dereferenced by the assembler
A0 00010400
- The first byte in the machine instruction is the opcode.
- The remaining part is the 32-bit hexadecimal address of var1.
00000000 .data
00000000 00000000 sum DWORD 0
00000000 .code
00000000 main proc
00000000 B8 00000008 mov eax, 8 00000005 83 C0 04 add eax, 4 00000008 A3 00000000 R mov sum, eax
Listing File

## Slide 11: Data Transfer Instructions: MOV Instruction
.data
count BYTE 100
wVal WORD 2
.code
mov bl,count
mov ax,wVal
mov count,al
mov al,wVal ; error
mov ax,count ; error
mov eax,count ; error
Move from source to destination.
Syntax:
    MOV destination, source
MOV instruction formats:
  Both operands must be the same size.
  Both operands cannot be memory operands.
  The (IP, EIP, or RIP) cannot be a destination operand.
Ex:
MOV reg,reg
MOV mem,reg
MOV reg,mem
MOV mem,imm
MOV reg,imm

## Slide 12: Data Transfer Instructions: MOV Instruction
Explain why each of the following MOV statements are invalid:
size mismatch
.data
bVal BYTE 100
bVal2 BYTE ?
wVal WORD 2
dVal DWORD 5
.code
mov ds,45
mov eax,wVal
mov eip,dVal
mov 25,bVal
mov bVal2,bVal
immediate move to DS not permitted
EIP cannot be the destination
immediate value cannot be destination
memory-to-memory move not permitted
Both operands must be the same size.
Both operands cannot be memory operands.
The (IP, EIP, or RIP) cannot be a destination operand.

## Slide 13: Data Transfer Instructions: MOV Instruction
Memory to Memory (problem):
  A single MOV instruction cannot be used to move data directly from one memory location to another.
  Instead, you must move
    the source operand’s value to a register
    before assigning its value to a memory operand:
.data
var1 WORD ?
var2 WORD ?
.code
mov ax,var1
mov var2,ax
Ex:
Notes: Sec09 Feb14th

## Slide 14: Data Transfer Instructions: MOV Instruction
.data
oneWord WORD 1234h
oneDword DWORD 12345678h
Overlapping Values
The same 32-bit register can be modified using differently sized data.
  When oneWord is moved to AX, it overwrites the existing value of AL.
  When oneDword is moved to EAX, it overwrites AX.
  When 0 is moved to AX, it overwrites the lower half of EAX.
.code
mov eax, 0
mov ax, oneWord ; EAX = 00001234h
mov eax, oneDword ; EAX = 12345678h
mov ax, 0 ; EAX = 12340000h
Notes: Sec 06, Feb 15

## Slide 15: Data Transfer Instructions: Zero & Sign Extension
Sign extension problem:
MOV cannot directly copy data from a smaller operand to a larger one
Workarounds:
Suppose count (unsigned, 16 bits) must be moved to ECX (32 bits).
Trick: Set ECX to zero and move count to CX:
What happens if we try the same approach with a signed integer equal to -16?
00000000000000000000000000000000
0000000000000001
cx
ch
cl
ecx
00000000000000000000000000000001
ecx

## Slide 16
00000000000000000000000000000000
0000000000000001
cx
ch
cl
ecx

## Slide 17: Data Transfer Instructions: Zero & Sign Extension
Sign extension problem:
What happens if we try the same approach with a signed integer equal to -16?

## Slide 19: Data Transfer Instructions: Zero & Sign Extension
Sign extension problem:
If we had filled ECX first with FFFFFFFFh and then copied signedVal to CX:
mov ecx,FFFFFFFFh
mov cx,signedVal ; ECX = FFFFFFF0h (-16)
MOVZX and MOVSX instructions to deal with both unsigned and signed integers.
11111111111111111111111111111111
1111111111110000
cx
ch
cl
ecx
11111111111111111111111111110000

## Slide 20: Data Transfer Instructions: Zero Extension (MOVZX )
The MOVZX instruction
When you copy a smaller value into a larger destination,
  the MOVZX instruction fills (extends) the upper half of the destination with zeros.
mov bl,10001111b
movzx ax,bl ; zero-extension
The destination must be a register.
ax
ah
al

## Slide 22: Data Transfer Instructions: Zero Extension (MOVZX )

## Slide 23: Data Transfer Instructions: Sign Extension (MOVSX )
The MOVSX instruction
It fills the upper half of the destination with a copy of the source operand's sign bit.
mov bl,10001111b
movsx ax,bl ; sign extension
The destination must be a register.
ax
ah
al

## Slide 24: Data Transfer Instructions: Sign Extension (MOVSX )
In the following example,
  the hexadecimal value moved to BX is A69B,
  so the leading “A” digit tells us that the highest bit is set.
mov bx, A69Bh
movsx eax,bx ; EAX = FFFFA69Bh
movsx edx,bl ; EDX = FFFFFF9Bh
movsx cx,bl ; CX = FF9Bh
Notes: TH, Sep-26, 4pm

## Slide 25: Data Transfer Instructions: Zero & Sign Extension
MOVZX vs. MOVSX
ax
ah
al
ax
ah
al
MOVZX
MOVSX

## Slide 27: Data Transfer Instructions: XCHG Instruction
XCHG exchanges the values of two operands.
  At least one operand must be a register.
  No immediate operands are permitted.
xchg ah,al ; exchange 8-bit regs
xchg ax,bx ; exchange 16-bit regs
xchg eax,ebx ; exchange 32-bit regs
xchg var1,bx ; exchange 16-bit mem op with BX
xchg var1,var2 ; error: two memory operands
Notes: Sec 03, Fe16

## Slide 29
Xchange items

## Slide 30: Data Transfer Instructions: XCHG Instruction
.data
var1 WORD 1000h
var2 WORD 2000h
.code
XCHG exchanges the values of two operands.
  At least one operand must be a register.
  No immediate operands are permitted.
mov ax,val1
xchg ax,val2
mov val1,ax

## Slide 31: Data Transfer Instructions: Direct-Offset Operands
.data
arrayB BYTE 10h,20h,30h,40h
.code
mov al,arrayB ; AL = 10h
mov al,arrayB+1 ; AL = 20h
A constant offset is added to a data label to produce an effective address (EA).
The address is dereferenced to get the value inside its memory location.
Why doesn't arrayB+1 produce 11h?
mov al,[arrayB+1] ; alternative notation
Notes: Sec-09, Feb-18

## Slide 32: Data Transfer Instructions: Direct-Offset Operands
.data
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov ax, [arrayW+2] ; AX = 2000h
mov ax, [arrayW+4] ; AX = 3000h
mov eax,[arrayD+4] ; EAX = 00000002h
Will the following statements assemble?
mov ax,[arrayW-2] ; ??
mov eax,[arrayD+16] ; ??

## Slide 34: Data Transfer Instructions: Direct-Offset Operands
.data
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov ax, [arrayD+0] ; AX = 2000h
mov ax, [arrayD+4] ; AX = 3000h
mov eax,[arrayD+8] ; EAX = 00000002h
Will the following statements assemble?
mov ax,[arrayW-2] ; ??
mov eax,[arrayD+16] ; ??

## Slide 36: Data Transfer Instructions: Direct-Offset Operands
Write a program that rearranges the values of three doubleword values in the following array as:
  1,2,3 ---------- 3, 1, 2.
  .data
  arrayD DWORD 1,2,3
Step 2: Exchange EAX with the THIRD array value and copy the value in EAX to the FIRST array position.
Step1: copy the FIRST value into EAX and exchange it with the value in the SECOND position.
xchg eax,[arrayD+8]
mov arrayD,eax
mov eax, arrayD
xchg eax, [arrayD+4]
LAB

## Slide 38: Data Transfer Instructions: Direct-Offset Operands
We want to write a program that adds the following three bytes:
.data
myBytes BYTE 80h,66h,0A5h
What is your evaluation of the following code?
mov al,myBytes
add al,[myBytes+1]
add al,[myBytes+2]
What is your evaluation of the following code?
movsx ax, myBytes
add ax, [myBytes+1]
add ax, [myBytes+2]
Any other possibilities?