## Slide 1: CSC 3210 Computer Organization and Programming
Chapter 7: Integer Arithmetic

## Slide 2: Outline
Shift and Rotate Instructions
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and Unpacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 3: Shift and Rotate Instructions
Bit shifting means to move bits right and left inside an operand
x86 processors provide a particularly set of instructions
These instructions affect the Overflow and Carry flags

## Slide 4: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions

## Slide 5: Logical Shift
There are two ways to shift an operand’s bits
  The first: logical shift, fills the newly created bit position with zero
Example:
    A byte is logically shifted one position to the right
    Each bit is moved to the next lowest bit position
    Note that bit 7 is assigned 0:
The lowest bit is shifted into the Carry flag

## Slide 6: Arithmetic Shift
  The Second: arithmetic shift, the newly created bit position is filled with
a copy of the original number’s sign bit
Example:
      Binary 11001111 has a 1 in the sign bit
      When shifted arithmetically 1 bit to the right, it becomes 11100111:

## Slide 9: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions

## Slide 10: SHL Instruction
The SHL (shift left) instruction
  Performs a logical left shift on the destination operand, filling the lowest bit with 0.
SHL reg,imm8
SHL mem,imm8
SHL reg,CL
SHL mem,CL
Same for all shift and rotate instructions: SHR, SAL, SAR, ROR, ROL, RCR, and RCL
- CL register can contain a shift count.

## Slide 12: SHL Instruction
The SHL (shift left) instruction
SHL reg,imm8
SHL mem,imm8
SHL reg,CL
SHL mem,CL
Example:
  BL is shifted once to the left.
  The highest bit is copied into the Carry flag and the lowest bit
position is assigned zero:
mov bl,8Fh ; BL = 10001111b
shl bl,1 ; CF = 1, BL = 00011110b

## Slide 13: SHL Instruction
When a value is shifted leftward multiple times,
  The Carry flag contains the last bit to be shifted out of the most significant bit (MSB)
Example:
  bit 7 does not end up in the Carry flag because it is replaced by bit 6 (a zero):
Similarly, when a value is shifted rightward multiple times,
  The Carry flag contains the last bit to be shifted out of the least significant bit (LSB)
mov al,10000000b
shl al,2 ; CF = 0, AL = 00000000b

## Slide 14: SHL Instruction
Fast Multiplication
mov dl,5
shl dl,1
Shifting left 1 bit multiplies a number by 2
Shifting left n bits multiplies the operand by 2n
  For example, 5 * 22 = 20
mov dl,5
shl dl,2 ; DL = 20

## Slide 15: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions

## Slide 16: SHR Instruction
The SHR (shift right) instruction performs a logical right shift on the destination operand
The highest bit position is filled with a zero.
Example,
  The 0 from the lowest bit in AL is copied into the Carry flag,
  And the highest bit in AL is filled with a zero:
mov al,0D0h ; AL = 11010000b
shr al,1 ; AL = 01101000b, CF = 0

## Slide 17: SHR Instruction
In a multiple shift operation,
  the last bit to be shifted out of position 0 (the LSB) ends up in the Carry flag:
mov al,00000010b
shr al,2 ; AL = 00000000b, CF = 1

## Slide 18: SHR Instruction
Fast Division
  Shifting right n bits divides the operand by 2n
mov dl,80
shr dl,1 ; DL = 40 ????
shr dl,2 ; DL = 10 ????

## Slide 19: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions

## Slide 20: SAL Instruction
SAL (shift arithmetic left) is identical to SHL
The lowest bit is assigned 0
The highest bit is moved to the Carry flag,
And the bit that was in the Carry flag is discarded:
If you shift binary 11001111 to the left by one bit,
  it becomes 10011110:

## Slide 21: SAR Instruction
SAR is identical to SHR
SAR (shift arithmetic right) performs a right arithmetic shift on the destination operand
The following example shows how SAR duplicates the sign bit.
  AL is negative before and after it is shifted to the right:
mov al,0F0h ; AL = 11110000b (-16?)
sar al,1 ; AL = 11111000b ( -8 ?) CF = 0
Notes: -80 = 10110000

## Slide 22: SAR Instruction
SAR is identical to SHR
mov dl,-80
sar dl,1 ; DL = -40 CF=?
sar dl,2 ; DL = -10 CF=?
Notes: -80 = 10110000

## Slide 23: Application
Indicate the hexadecimal value of AL after each shift:
mov al,6Bh
shr al,1 a.
shl al,3 b.
mov al,8Ch
sar al,1 c.
sar al,3 d.
35h
A8h
C6h
F8h

## Slide 24: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions

## Slide 25: ROL Instruction
ROL (rotate) shifts each bit to the left
The highest bit is copied into both the Carry flag and into the lowest bit
No bits are lost
mov al,11110000b
rol al,1 ; AL = 11100001b, CF = ?
Example1:

## Slide 27: ROL Instruction
ROL (rotate) shifts each bit to the left
mov al,40h ; AL = 01000000b
rol al,1 ; AL = 10000000b, CF = 0
rol al,1 ; AL = 00000001b, CF = 1
rol al,1 ; AL =00000010b, CF = 0
Example2:

## Slide 28: ROL Instruction
Multiple Rotations
  When using a rotation count greater than 1,
  Carry flag contains the last bit rotated out of the MSB position:
mov al,00100000b
rol al,3 ; CF = 1, AL = 00000001b

## Slide 29: ROL Instruction
Exchanging Groups of Bits (Application)
  You can use ROL to exchange the upper (bits 4–7) and lower (bits 0–3) halves of a byte
mov al,26h
rol al,4 ; AL = 62h

## Slide 30: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions

## Slide 31: ROR Instruction
ROR (rotate right) shifts each bit to the right
The lowest bit is copied into both the Carry flag and into the highest bit
No bits are lost
mov al,01h ; AL = 00000001b
ror al,1 ; AL = 10000000b, CF = 1
ror al,1 ; AL = 01000000b, CF = 0
Example1:

## Slide 32: ROR Instruction
ROR (rotate right) shifts each bit to the right
mov dl,3Fh
ror dl,4 ; DL = F3h
Example2:

## Slide 33: ROR Instruction
Multiple Rotations
  When using a rotation count greater than 1,
  Carry flag contains the last bit rotated out of the LSB position:
mov al,00000100b
ror al,3 ; AL = 10000000b, CF = 1

## Slide 34: Application
mov al,6Bh
ror al,1 a.
rol al,3 b.
Indicate the hexadecimal value of AL after each rotation:
B5h
ADh

## Slide 35: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions

## Slide 36: RCL Instruction
RCL (rotate carry left) shifts each bit to the left
  Copies the Carry flag to the least significant bit
  Copies the most significant bit to the Carry flag
clc ; CF = 0 , CLC instruction clears the Carry flag
mov bl,88h ; CF = 0 , BL= 10001000b
rcl bl,1 ; CF = 1 , BL= 00010000b
rcl bl,1 ; CF = 0 , BL= 00100001b

## Slide 38: RCR Instruction
RCR (rotate carry right) shifts each bit to the right
  Copies the Carry flag to the most significant bit
  Copies the least significant bit to the Carry flag
stc ; CF = 1 , STC to set the Carry flag
mov ah,10h ; CF = 1 , AH = 00010000b
rcr ah,1 ; CF = 0 , AH = 10001000b

## Slide 39: Application
stc
mov al,6Bh
rcr al,1 a.
rcl al,3 b.
Indicate the hexadecimal value of AL after each rotation:
B5h
AEh

## Slide 40: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions: See the book

## Slide 41: Outline
Shift and Rotate Instructions
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and Unpacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 42: Multiplication and Division Instructions
MUL Instruction
IMUL Instruction
DIV Instruction
Signed Integer Division
CBW, CWD, CDQ Instructions
IDIV Instruction
Implementing Arithmetic Expressions

## Slide 43: MUL Instruction
In 32-bit mode, MUL (unsigned multiply) instruction multiplies an 8-, 16-, or 32-bit operand by either AL, AX, or EAX.
The instruction formats are:
Multiplier operands
Notes: EDX: The Data Register
Of the seven remaining general-purpose registers, the data register, EDX, is most closely tied to the accumulator. Instructions that deal with over sized data items, such as multiplication, division, CWD, and CDQ, store the most significant bits in the data register and the least significant bits in the accumulator. In a sense, the data register is the 64-bit extension of the accumulator. The data register also plays a part in IO instructions. In this case, the accumulator holds the data to read or write from the port, and the data register holds the port address.
EAX - All major calculations take place in EAX, making it similar to a dedicated accumulator register.
EDX - The data register is the an extension to the accumulator. It is most useful for storing data related to the accumulator's current calculation.
ECX - Like the variable i in high-level languages, the count register is the universal loop counter.
EDI - Every loop must store its result somewhere, and the destination index points to that place. With a single-byte STOS instruction to write data out of the accumulator, this register makes data operations much more size-efficient.
ESI - In loops that process data, the source index holds the location of the input data stream. Like the destination index, EDI has a convenient one-byte instruction for loading data out of memory into the accumulator.
ESP - ESP is the sacred stack pointer. With the important PUSH, POP, CALL, and RET instructions requiring it's value, there is never a good reason to use the stack pointer for anything else.
EBP - In functions that store parameters or variables on the stack, the base pointer holds the location of the current stack frame. In other situations, however, EBP is a free data-storage register.
EBX - In 16-bit mode, the base register was useful as a pointer. Now it is completely free for extra storage space.

## Slide 45: MUL Instruction
The instruction formats are:
Because the destination operand is
twice the size of the multiplicand and multiplier, overflow cannot occur.
Multiplier operands
The colon (:) means concatenation. This means that DX are the bits 16-31 and AX are bits 0-15 of the input number
over sized data
Notes: EDX: The Data Register
Of the seven remaining general-purpose registers, the data register, EDX, is most closely tied to the accumulator. Instructions that deal with over sized data items, such as multiplication, division, CWD, and CDQ, store the most significant bits in the data register and the least significant bits in the accumulator. In a sense, the data register is the 64-bit extension of the accumulator. The data register also plays a part in IO instructions. In this case, the accumulator holds the data to read or write from the port, and the data register holds the port address.
EAX - All major calculations take place in EAX, making it similar to a dedicated accumulator register.
EDX - The data register is the an extension to the accumulator. It is most useful for storing data related to the accumulator's current calculation.
ECX - Like the variable i in high-level languages, the count register is the universal loop counter.
EDI - Every loop must store its result somewhere, and the destination index points to that place. With a single-byte STOS instruction to write data out of the accumulator, this register makes data operations much more size-efficient.
ESI - In loops that process data, the source index holds the location of the input data stream. Like the destination index, EDI has a convenient one-byte instruction for loading data out of memory into the accumulator.
ESP - ESP is the sacred stack pointer. With the important PUSH, POP, CALL, and RET instructions requiring it's value, there is never a good reason to use the stack pointer for anything else.
EBP - In functions that store parameters or variables on the stack, the base pointer holds the location of the current stack frame. In other situations, however, EBP is a free data-storage register.
EBX - In 16-bit mode, the base register was useful as a pointer. Now it is completely free for extra storage space.

## Slide 46: MUL Instruction
The Carry flag indicates whether or not the upper half of the product contains significant digits (?)
Because the destination operand is
twice the size of the multiplicand and multiplier, overflow cannot occur.
Notes: TU Oct-24,9:30am
Sec06, April3rd

## Slide 47: MUL: Example1
Example1: 100h * 2000h, unsigned 16-bit operands:
.data
val1 WORD 2000h
val2 WORD 0100h
.code
mov ax,val1
mul val2 ; DX:AX = 00200000h, CF=1
The Carry flag indicates whether or not the upper half of the product contains significant digits (?)
Because the destination operand is
twice the size of the multiplicand and multiplier, overflow cannot occur.
Result = 200000h

## Slide 48: MUL: Example2
12345h * 1000h, using 32-bit operands:
mov eax,12345h
mov ebx,1000h
mul ebx ; EDX:EAX = 0000000012345000h, CF=0
The Carry flag indicates whether or not the upper half of the product contains significant digits (?)
Result = 12345000h
Notes: Wed 3pm, Oct-23

## Slide 49: MUL: Example3
mov ax,1234h
mov bx,100h
mul bx
What will be the hexadecimal values of DX, AX, and the Carry flag after the following instructions execute?
DX = 0012h, AX = 3400h, CF = 1
Result = 123400h

## Slide 50: MUL: Example4
mov eax,00128765h
mov ecx,10000h
mul ecx
What will be the hexadecimal values of EDX, EAX, and the Carry flag after the following instructions execute?
EDX = 00000012h, EAX = 87650000h, CF = 1
Result = 1287650000h

## Slide 51: Multiplication and Division Instructions
MUL Instruction
IMUL Instruction
DIV Instruction
Signed Integer Division
CBW, CWD, CDQ Instructions
IDIV Instruction
Implementing Arithmetic Expressions
Notes: Sec09 Apr04

## Slide 52: IMUL Instruction
IMUL (signed integer multiply ) multiplies an 8-, 16-, or 32-bit signed operand by either AL, AX, or EAX
Preserves the sign of the product by sign-extending it into the upper half of the destination register
x86 instruction set supports three formats for the IMUL instruction:
  One operand, two operands, and three operands.
Notes: http://www.c-jump.com/CIS77/MLabs/M11arithmetic/lecture.html#M11_0060_imul_instruction

## Slide 53: IMUL Instruction
IMUL (signed integer multiply ) multiplies an 8-, 16-, or 32-bit signed operand by either AL, AX, or EAX
  The one-operand format, the multiplier and multiplicand are the same size and the product is twice their size
Multiplier operands
Notes: http://www.c-jump.com/CIS77/MLabs/M11arithmetic/lecture.html#M11_0060_imul_instruction

## Slide 54: IMUL Instruction
The two-operand version of the IMUL instruction in 32-bit mode
  Stores the product in the first operand, which must be a register
  The second operand (the multiplier) can be a register, a memory operand, or an immediate value
Following are the 16-bit formats:
Product
multiplier

## Slide 55: IMUL Instruction
The two-operand version of the IMUL instruction in 32-bit mode
The two-operand formats truncate the product to the length of the destination
If significant digits are lost,
  the Overflow and Carry flags are set
  Be sure to check one of these flags after performing an IMUL operation with two operands
The 32-bit operand types showing that the multiplier can be
  a 32-bit register, a32-bit memory operand, or an immediate value (8 or 32 bits):

## Slide 56: IMUL Instruction
The three-operand formats in 32-bit mode
  Store the product in the first operand
  The second operand can be
    a 16-bit register or memory operand, which is multiplied by the third operand,
    the third operand can be an 8- or 16-bit immediate value:
Product
Multiplicand
Multiplier

## Slide 57: IMUL Instruction
A 32-bit register or memory operand can be multiplied by
  an 8- or 32-bit immediate value:
    Truncate the product to the length of the destination, If significant digits are lost,
      the Overflow and Carry flags are set
      Be sure to check one of these flags after performing an IMUL operation with two operands
Product
Multiplicand
Multiplier

## Slide 58: IMUL: Example1
multiply 48 * 4, using 8-bit operands:
mov al,48
mov bl,4
imul bl ; AX = 00C0h, OF=1
OF=1 because AH is not a sign extension of AL.
The following instructions demonstrate one-operand formats:
Preserves the sign of the product by sign-extending it into the upper half of the destination register
Multiplier operands
Notes: 4 X 48 = 192 (Range of sign number is -128 to -1, so this out of range and OF=1)

## Slide 59: IMUL: Example2
Multiply 4,823,424 * -423:
mov eax,4823424
mov ebx,-423
imul ebx ; EDX:EAX = FFFFFFFF86635D80h, OF=0
OF=0 because EDX is a sign extension of EAX.
The following instructions demonstrate one-operand formats:
Preserves the sign of the product by sign-extending it into the upper half of the destination register
Multiplier operands
Notes: 4823424 X 423 = 2040308352
2^32 / 2 =2147483648

## Slide 60: IMUL: Example3
mov ax,8760h
mov bx,100h
imul bx
What will be the hexadecimal values of DX, AX, and the Carry flag after the following instructions execute?
DX = FF87h, AX = 6000h, OF = 1
The following instructions demonstrate one-operand formats:
Preserves the sign of the product by sign-extending it into the upper half of the destination register
Product = 876000h
Multiplier operands
DX is not a sign extension
Notes: 8760h X 100= 0x876000
2^16/2 = 32768
0x876000 = 8871936 (decemal)

## Slide 61: IMUL: Example4
The following instructions demonstrate two-operand formats:
.data
word1 SWORD 4
dword1 SDWORD 4
.code
mov ax,-16 ; AX = -16
mov bx,2 ; BX = 2
imul bx,ax ; BX = -32
imul bx,2 ; BX = -64
imul bx,word1 ; BX = -256
mov eax,-16 ; EAX = -16
mov ebx,2 ; EBX = 2
imul ebx,eax ; EBX = -32
imul ebx,2 ; EBX = -64
imul ebx,dword1 ; EBX = -256
Product

## Slide 62: IMUL: Example5
The following instructions demonstrate two-operand formats:
The two-operand and three-operand IMUL instructions use a destination operand that is the same size as the multiplier.
Therefore, it is possible for signed overflow to occur.
mov ax,-32000
imul ax,2 ; OF = 1
signed overflow because 64,000 cannot fit within the 16-bit destination operand
216= 65536 (UNSIGNED) : 0 to 65535
215= 32768(SIGNED ) : -1 to -32768 and 0 to 32767

## Slide 63: IMUL: Example6
The two-operand and three-operand IMUL instructions use a destination operand that is the same size as the multiplier.
Therefore, it is possible for signed overflow to occur.
The following instructions demonstrate three-operand formats:
.data
word1 SWORD 4
dword1 SDWORD 4
.code
imul bx,word1,-16 ; BX = word1 * -16
imul ebx,dword1,-16 ; EBX = dword1 * -16
imul ebx,dword1,-2000000000 ; signed overflow!
Product
Multiplicand
Multiplier

## Slide 64: Multiplication and Division Instructions
MUL Instruction
IMUL Instruction
DIV Instruction
Signed Integer Division
CBW, CWD, CDQ Instructions
IDIV Instruction
Implementing Arithmetic Expressions
Notes: TU, OCT24,4P

## Slide 65: DIV Instruction
The DIV (unsigned divide) instruction performs 8-bit, 16-bit, and 32-bit division on unsigned integers
A single operand is supplied (register or memory operand), which is assumed to be the divisor
Instruction formats:
divisor
DIV reg/mem8
DIV reg/mem16
DIV reg/mem32

## Slide 66: DIV Instruction
The DIV (unsigned divide) instruction performs 8-bit, 16-bit, and 32-bit division on unsigned integers
divisor
DIV reg/mem8
DIV reg/mem16
DIV reg/mem32

## Slide 67: DIV: Example1
The following instructions perform 8-bit unsigned division (83h/2),
  producing a quotient of 41h
  and a remainder of 1
mov ax,0083h ; dividend
mov bl,2 ; divisor
div bl ; AL = 41h, AH = 01h

## Slide 68: DIV: Example2
Divide 8003h by 100h, using 16-bit operands:
mov dx,0 ; clear dividend, high
mov ax,8003h ; dividend, low
mov cx,100h ; divisor
div cx ; AX = 0080h, DX = 3

## Slide 69: DIV: Example3
Same division, using 32-bit operands:
mov edx,0008h ; dividend, high
mov eax,00300020h ; dividend, low
mov ecx,100h ; divisor
div ecx ; EAX = , DX =
000800300020h

## Slide 70: DIV: Example4
mov dx,0087h
mov ax,6000h
mov bx,100h
div bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:
DX = , AX =
Quotient = 8760, Rem = 0
Use Visual Studio
00876000h

## Slide 71: DIV: Example5
mov dx,0087h
mov ax,6002h
mov bx,10h
div bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:
Answer: Divide Overflow
If a division operand produces a quotient that will not fit into the destination operand, a divide overflow condition results
- All arithmetic status flag values are undefined after executing DIV and IDIV

## Slide 72: DIV: Division by Zero
To prevent division by zero, test the divisor before dividing:
mov ax,dividend
mov bl,divisor
cmp bl,0 ; check the divisor
je NoDivideZero ; zero? display error
div bl ; not zero: continue
.
.
NoDivideZero: ;(display "Attempt to divide by zero")

## Slide 73: Multiplication and Division Instructions
MUL Instruction
IMUL Instruction
DIV Instruction
Signed Integer Division
CBW, CWD, CDQ Instructions
IDIV Instruction
Implementing Arithmetic Expressions

## Slide 74: Signed Integer Division (IDIV)
Signed integers MUST be sign-extended before division takes place
  Fill high byte/word/doubleword with a copy of the low byte/word/doubleword's sign bit
Example: The high byte contains a copy of the sign bit from the low byte:
How to do sign-extension 🤔?
  sign bit

## Slide 75: CBW, CWD, CDQ Instructions
The CBW, CWD, and CDQ instructions provide important sign-extension operations:
  CBW (convert byte to word) extends AL into AH
  CWD (convert word to doubleword) extends AX into DX
  CDQ (convert doubleword to quadword) extends EAX into EDX
Example:
    .data
    dwordVal SDWORD -101 ; FFFFFF9Bh
    .code
    mov eax,dwordVal
    cdq ; EDX:EAX = FFFFFFFFFFFFFF9Bh

## Slide 76: IDIV Instruction
IDIV (signed divide) performs signed integer division
Same syntax and operands as DIV instruction
Example1: 8-bit division of –48 by 5
mov al,-48
cbw ; extend AL into AH
mov bl,5
idiv bl ; AL = -9, AH = -3

## Slide 77: IDIV Examples
Example3: 32-bit division of –48 by 5
mov eax,-48
cdq ; extend EAX into EDX
mov ebx,5
idiv ebx ; EAX = -9, EDX = -3
Example2: 16-bit division of –48 by 5
mov ax,-48
cwd ; extend AX into DX
mov bx,5
idiv bx ; AX = -9, DX = -3

## Slide 78: IDIV Examples
mov ax,0FDFFh ; -513
cwd
mov bx,100h
idiv bx
Example4: What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:
DX = FFFFh (-1), AX = FFFEh (-2)

## Slide 79: Unsigned Arithmetic Expressions
Some good reasons to learn how to implement integer expressions:
  Learn how do compilers do it
  Test your understanding of MUL, IMUL, DIV, IDIV
  Check for overflow (Carry and Overflow flags)

## Slide 80: Unsigned Arithmetic Expressions
Example1: var4 = (var1 + var2) * var3
; Assume unsigned operands
A good reason for checking the Carry flag after executing MUL is to know whether the upper half
of the product can safely be ignored.

## Slide 81: Unsigned Arithmetic Expressions
Example1: var4 = (var1 + var2) * var3
; Assume unsigned operands
mov eax,var1
add eax,var2 ; EAX = var1 + var2
mul var3 ; EAX = EAX * var3
jc TooBig ; check for carry
mov var4,eax ; save product
A good reason for checking the Carry flag after executing MUL is to know whether the upper half
of the product can safely be ignored.

## Slide 82
Example2: eax = (-var1 * var2) + var3
; Assume signed operands
Unsigned Arithmetic Expressions

## Slide 83
Example2: eax = (-var1 * var2) + var3
; Assume signed operands
mov eax,var1
neg eax
imul var2
jo TooBig ; check for overflow
add eax,var3
jo TooBig ; check for overflow
Unsigned Arithmetic Expressions

## Slide 84: Unsigned Arithmetic Expressions
Example3: var4 = (var1 * 5) / (var2 – 3)
; Assume unsigned operands
Do not modify any variables other than var4:
Notes: ?

## Slide 85: Unsigned Arithmetic Expressions
Example3: var4 = (var1 * 5) / (var2 – 3)
mov eax,var1 ; left side
mov ebx,5
mul ebx ; EDX:EAX = product
mov ebx,var2 ; right side
sub ebx,3
div ebx ; EAX = quotient
mov var4,eax
; Assume unsigned operands
Do not modify any variables other than var4:
Notes: ?

## Slide 86
Example4: var4 = (var1 * -5) / (-var2 / var3);
Sometimes it's easiest to calculate the right-hand term of an expression first.
Unsigned Arithmetic Expressions
; assume signed 32-bit integers
Var1=-2
Var2=20
Var3=2

## Slide 87
Example4: var4 = (var1 * -5) / (-var2 / var3);
mov eax,var2 ; begin right side
neg eax
cdq ; sign-extend dividend
idiv var3 ; EDX = remainder
mov ebx,eax ; EBX = right side
mov eax,-5 ; begin left side
imul var1 ; EDX:EAX = left side
idiv ebx ; final division
mov var4,eax ; quotient
Sometimes it's easiest to calculate the right-hand term of an expression first.
Unsigned Arithmetic Expressions
; assume signed 32-bit integers
Var1=-2
Var2=20
Var3=2

## Slide 88: Unsigned Arithmetic Expressions
Example5: Implement the following expression using signed 32-bit integers.
Do not modify any variables other than var3:
var3 = (var1 * -var2) / (var3 – ebx)

## Slide 89: Unsigned Arithmetic Expressions
mov eax,var1
mov edx,var2
neg edx
imul edx ; left side: EDX:EAX
mov ecx,var3
sub ecx,ebx
idiv ecx ; EAX = quotient
mov var3,eax
Example5: Implement the following expression using signed 32-bit integers.
Do not modify any variables other than var3:
var3 = (var1 * -var2) / (var3 – ebx)

## Slide 90: Outline
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction See the book
ASCII and Unpacked Decimal Arithmetic See the book
Packed Decimal Arithmetic See the book

## Slide 91: Extended Addition and Subtraction
Extended precision addition and subtraction is the technique of
  adding and subtracting numbers having an almost unlimited size
  In assembly language, the ADC instruction is well suited to this type of operation
How about subtraction?
    the SBB instruction is well suited to this type of operation
mov al,0FFh
add al,0FFh ; AL = FEh 🙄
mov eax,1
sub eax,2 ;EAX= ?